## Slide 1
Tank Inspection Copilot
Screen-by-Screen Validation Deck
29 screens · April 2026
Screen status key
NEW
Screen designed and built this project
UPDATED
Existing screen enhanced with new functionality
(no badge) — existing screen, unchanged

## Slide 2
Screen 01
Home
Landing screen — entry point for all inspection activity
01 / 29
PURPOSE
• Gives the inspector a one-glance summary of the active draft and quick-start buttons.
KEY ELEMENTS
• Inspection header — site, tank ID, inspection type badge
• Open draft metrics — Tank ID · Defect count · Surfaces completed / total
• Start New Inspection button → Inspection Setup flow
• Resume Draft Inspection → Tank Overview
• View Past Inspections (placeholder)
DESIGN INTENT
• No authentication required for field use. Session auto-persisted to localStorage.

## Slide 3
Screen 02
Inspection Setup
Define field context before capture begins
02 / 29
PURPOSE
• Captures the session metadata that stamps every defect record.
INPUTS
• Site — free text (e.g. SLNG Terminal)
• Client — optional free text
• Tank ID — e.g. TK-201
• Inspection type — Routine / External / Internal / Special
BEHAVIOUR
• Inspector name and date auto-filled from device context.
• Continue → Tank Profile. Save Draft → Home.

## Slide 4
Screen 03
Tank Profile
Physical dimensions and design standard — tank-level only
03 / 29
PURPOSE
• Records the tank's design basis. Used as reference for all geometry calculations downstream.
SECTIONS
• Design standard — API 650 / API 653 / Other (three-button toggle)
• Dimensions — Diameter (m), Total height (m), Nominal capacity m³ (optional)
• Construction type — Roof type (5 options) and Foundation type (3 options)
API 650 VS API 653 NOTE
• API 650 = new construction standard. API 653 = in-service inspection standard.
• Select the code the tank was originally designed and built to.
• Surface geometry (courses, plate width) is defined per-surface in dedicated Setup screens.

## Slide 5
Screen 04
Tank Orientation
GPS location and azimuth reference — defines 0° for all shell locations
04 / 29
PURPOSE
• Establishes the coordinate origin for shell azimuth measurements.
GPS SECTION
• Latitude / Longitude entry (decimal degrees)
• Use Device GPS button — one-tap capture with status feedback
AZIMUTH REFERENCE SECTION
• True North — 0° fixed to geographic north, no physical marker required
• Physical Marker — inspector identifies a fixed feature on the shell as the 0° anchor
→ Marker type (painted mark / Nozzle N1 / stairway / other)
→ Description field (how to find it on site)
→ Bearing from True North (°)
• Compass rose preview — green dot at 0° for True North; orange REF dot at bearing for Physical Marker

## Slide 6
Screen 05
Tank Overview
Surface selector — entry point for each inspectable area
05 / 29
PURPOSE
• Central hub after setup. Inspector chooses which surface to inspect next.
SURFACE CARDS (5 SURFACES)
• Bottom — Floor plate matrix and annular band
• Shell — Unwrapped cylinder, courses and plates
• Roof — Polar sector grid, apex to outer edge
• Annular ring — Circumferential band at shell junction
• Nozzle area — Clock-face map per nozzle / manway
STATUS BADGES PER CARD
• Setup required (amber) — geometry not yet defined, setup screen will appear first
• Tap to inspect — configured, no defects yet
• X defects — defects recorded but surface not complete
• Complete (teal) — surface marked done

## Slide 7
Screen 06
Shell Setup
NEW
Define shell course and plate geometry before inspection
06 / 29
PURPOSE
• Entered every time the inspector opens the Shell surface — pre-filled on revisit.
TANK REFERENCE CARD (READ-ONLY)
• Shows diameter, height, and computed circumference for reference.
COURSE GEOMETRY INPUTS
• Number of shell courses — e.g. 8
• Standard plate width circumferential (mm) — API 650 minimum 1 800 mm
DERIVED LAYOUT (COMPUTED, NOT ENTERED)
• Standard course height = floor(total height mm ÷ courses)
• Top course height = remainder (shown amber if differs)
• Plates per course = floor(circumference ÷ plate width) + 1 closure plate
• Closure plate width = circumference − n × plate width
SEAM LAYOUT INPUTS
• Course 1 first vertical seam azimuth (°) — from drawing
• Seam offset rule — ½ plate (2-course repeat) / ⅓ plate (3-course repeat) / Custom
• Generated course table — C1…Cn with z-range and seam origin per course
• Convention: ½ plate = C1/C3/C5 align, C2/C4/C6 shift +½ plate span. NOT cumulative.

## Slide 8
Screen 07
Shell Map
NEW
Unwrapped cylinder — tap to select plate location
07 / 29
PURPOSE
• Geometry-driven SVG of the full shell surface. Inspector taps a cell to record a defect location.
AXES
• X-axis — azimuth 0°–360°. Tick labels at every 45°.
• Y-axis — courses C1 (bottom) to Cn (top). Each row labelled: course number, height (mm), seam origin (°).
VISUAL FEATURES
• Per-course staggered vertical seam lines — shows the interlacing between adjacent courses
• Alternating row backgrounds (odd/even course shading)
• Dashed green reference line at 0° and at 360° wrap boundary
• Red defect dots at correct plate × course position
• Teal highlight on selected cell
• Zoom control — five steps (10/16/24/36/52 px per plate column)
TAP BEHAVIOUR
• Click → polar math → (plateIdx, courseNum) accounting for per-course seam offset
• Location summary shows: Course · Plate · Azimuth (°) · Elevation range (mm)
• Coordinate system: canonical (θ_deg, z_mm); plate/course is derived label

## Slide 9
Screen 08
Roof Setup
NEW
Define roof polar sector grid before inspection
08 / 29
PURPOSE
• Entered every time the inspector opens the Roof surface — pre-filled on revisit.
INPUTS
• Radial sectors — angular divisions. Typical: 8 for small tanks, 12–16 for large.
Each sector = 360 ÷ sectors degrees. Auto-calculated and shown.
• Concentric rings — radial zones. Typical: 4–6 rings.
Ring 1 = near apex (centre). Ring n = outer edge.
• Apex height above shell top (m) — optional, for cone/dome roofs
LIVE POLAR GRID PREVIEW
• SVG dartboard diagram updates as you change sector/ring counts.
• Shows sector count × ring count = total inspection zones.
• 0° reference line at top (north), clockwise convention.

## Slide 10
Screen 09
Roof Map
NEW
Polar sector × ring grid — tap to select zone
09 / 29
PURPOSE
• Top-down polar view of the roof. Inspector taps a sector-ring zone to record a defect.
ADDRESS SYSTEM
• x = sectorIdx (1 .. sectorCount, starts at 0° clockwise)
• y = ringIdx (1 = apex/innermost, n = outer edge)
• Location summary shows: Sector S{x} · Ring R{y} · Azimuth range
VISUAL FEATURES
• SVG arc-path cells — each cell is a true pie-slice annular segment
• Alternating ring shading (light / lighter green bands)
• Azimuth labels at each sector boundary around the outside
• Bold 0° reference line at top, clockwise
• R1..Rn labels along the right side
• Red defect dots at cell midpoint
• Teal ring highlight on selected cell

## Slide 11
Screen 10
Annular Ring Setup
NEW
Define annular ring width before inspection
10 / 29
PURPOSE
• Entered every time the inspector opens the Annular surface — pre-filled on revisit.
INPUT
• Annular ring width (mm) — inward from shell wall. API 650 §5.5 minimum 600 mm for ≥30 m tanks.
• Tank reference — diameter and outer circumference shown from Tank Profile.
TOP-VIEW DIAGRAM (STATIC PREVIEW)
• Circular SVG showing tank floor (inner), annular band (teal), shell wall (outer).
• 0°/90°/180°/270° azimuth labels. 0° reference tick at top.
• Annular width label shown on the diagram.
CONVENTION
• Annular ring is inspected as a top-down circular band, NOT an unwrapped strip.
• 36 × 10° zones for defect addressing.

## Slide 12
Screen 11
Annular Ring Map
NEW
Top-view circular band — 36 × 10° tappable zones
11 / 29
PURPOSE
• Interactive top-down view of the annular band. Inspector taps a 10° zone to record a defect.
ADDRESS SYSTEM
• x = azimuth zone index (1 .. 36, zone 1 = 0°–10°, zone 36 = 350°–360°)
• y = 1 (single band — no radial subdivision)
• Location summary shows: Zone number · Azimuth range (°)
VISUAL FEATURES
• 36 arc-path segments forming the complete ring
• Alternating green shading between adjacent zones
• Tank floor shown as non-interactive inner circle
• Shell wall shown as thick outer ring
• 0°/90°/180°/270° azimuth labels. 0° reference tick at top.
• Annular width (mm) label from config
• Red defect dots at zone midpoint. Teal fill on selected zone.
• Tap outside the band → no selection (inner floor and outer shell are non-tappable)

## Slide 13
Screen 12
Nozzle Registry
NEW
Register all nozzles and manways before inspection
12 / 29
PURPOSE
• One-time setup (or edit) of the nozzle inventory for the tank.
PER-NOZZLE FIELDS
• ID — e.g. N1, N2, M1 (manway)
• Type — inlet / outlet / vent / drain / manway / instrument / other
• Azimuth (°) — circumferential position on shell
• Elevation from datum (mm) — height from tank base
• Nominal bore diameter (mm)
• Description — optional free text (how to find it on site)
LIST MANAGEMENT
• Nozzles displayed as compact rows sorted by ID.
• + Add button opens inline form. Remove button per row.
• Continue enabled only when at least one nozzle is registered.

## Slide 14
Screen 13
Nozzle List
NEW
Select a nozzle to inspect
13 / 29
PURPOSE
• Shows all registered nozzles. Inspector taps one to open its clock-face inspection map.
CARD PER NOZZLE
• Shows: ID · type · azimuth · elevation · bore diameter · description
• Status badge — defect count (red) or 'Not started'
NAVIGATION
• Tap a nozzle → sets selectedNozzle state → opens Nozzle Clock Map
• Edit Nozzle Registry button → returns to Nozzle Registry to add/remove nozzles
• Back to Overview → Tank Overview

## Slide 15
Screen 14
Nozzle Clock Map
NEW
Clock-face inspection zone per nozzle — 12 positions × 3 rings
14 / 29
PURPOSE
• Per-nozzle top-down view centred on the nozzle CL. Inspector taps a clock position + ring to locate a defect.
ADDRESS SYSTEM
• x = clock position (1 = 12 o'clock, 2 = 1 o'clock … 12 = 11 o'clock)
• y = ring index (1 = 0–50 mm, 2 = 50–100 mm, 3 = 100–150 mm from nozzle CL)
• Location summary shows: Nozzle ID · Clock position · Distance ring
VISUAL FEATURES
• SVG arc-path cells — 12 sectors × 3 rings = 36 inspection cells
• Nozzle header bar — ID, type, azimuth, bore diameter
• 12 o'clock = top, bold reference line. Clockwise. Clock labels around outside.
• Ring radius labels in mm (50 / 100 / 150)
• Nozzle bore shown as dashed inner circle (diameter to scale)
• Red defect dots. Per-nozzle defect filtering (plateId === nozzle.id).
INSPECTION ZONE
• 150 mm radius from nozzle CL — per API 653 nozzle inspection convention.

## Slide 16
Screen 15
Location Mode
Choose how to specify the defect location
15 / 29
PURPOSE
• Lets the inspector pick the most convenient location entry method for current conditions.
THREE MODES
• Tap on Grid Map (Recommended) — tap the surface map directly
• Manual X,Y Entry — type partition numbers; useful when reading from a checklist
• Plate ID Entry — search a plate number from the drawing register
CONTEXT
• For Shell, Roof, Annular and Nozzle surfaces the dedicated map is the primary method.
• Manual and Plate ID are available as fallbacks for any surface.

## Slide 17
Screen 16
Manual Entry
Type X, Y partition coordinates directly
16 / 29
PURPOSE
• Fallback entry for situations where map interaction is impractical (e.g. limited screen space, working from paper checklist).
INPUTS
• X partition — column number
• Y partition — row number
• Live validation — shows green 'Valid partition' or red 'Outside inspectable surface'.
ACTIONS
• Preview on Map — navigates to the map screen with the typed coordinates highlighted
• Confirm Location — proceeds to Location Confirmation

## Slide 18
Screen 17
Plate ID Picker
Search and select a plate by its drawing ID
17 / 29
PURPOSE
• Allows inspectors working from a plate register drawing to locate defects by plate label.
INPUTS
• Search field — filters plate list by ID prefix as you type
• Plate cards — Plate ID · subzone description · grid coordinates badge
• Show on Map — opens the map with the selected plate highlighted
NOTE
• Currently pre-populated with sample plate data. In production, loaded from the tank drawing register.

## Slide 19
Screen 18
Location Confirmation
Review and lock the defect location before typing
18 / 29
PURPOSE
• Prevents accidental mislocations. Inspector reviews the location summary and the map highlight before committing.
LOCATION SUMMARY CARD
• Shell — Course · Plate · Azimuth (°) · Elevation range (mm)
• Roof — Sector · Ring · Azimuth range
• Annular — Zone number · Azimuth range
• Nozzle — Nozzle ID · Clock position · Distance ring
• Other — X · Y · Grid ID · Plate ID
MAP MINI-VIEW
• Same map component as the selection screen (Shell / Roof / Annular / Nozzle / Grid), read-only, selected cell highlighted.
ACTIONS
• Use This Location → Defect Type screen
• Edit Location → returns to the appropriate location entry screen

## Slide 20
Screen 19
Defect Type
Choose the defect category
19 / 29
PURPOSE
• First classification step. Sets the defect type which drives which measurement fields appear.
OPTIONS
• Corrosion
• Crack
• Deformation
• Coating Failure
• Leakage
• Weld Defect
• Patch / Repair Observation
• Other

## Slide 21
Screen 20
Defect Details
UPDATED
Severity, extent, weld flag and description — weld seam selector added
20 / 29
PURPOSE
• Captures classification metadata for the defect.
INPUTS
• Subtype — free text (e.g. 'pitting', 'general', 'inter-granular')
• Severity — Minor / Moderate / Severe (three-button toggle)
• Extent — single cell / multi-cell region / edge/annular
NEW — AT A WELD SEAM? SELECTOR
• Shown for all surfaces. Options filtered by surface context:
Shell / Bottom / Roof: Field (no weld) · Vertical seam (VS) · Horizontal seam (HS) · Nozzle toe
Annular: Field · Annular seam · Nozzle toe
Nozzle: Field · Nozzle toe
• Default = 'Field (no weld)' — no extra steps for standard plate defects.
• Rationale: weld location is derivable from plate address — no separate Weld surface needed.
• Description — free-text field notes

## Slide 22
Screen 21
Measurements
Quantitative readings — fields driven by defect type
21 / 29
PURPOSE
• Records the measurement data needed for API 653 fitness-for-service assessment.
FIELDS SHOWN PER DEFECT TYPE
• Corrosion / General — UT thickness (mm) · Minimum thickness (mm) · Pit depth (mm)
• Crack — Crack length (mm) · Crack width (mm)
• Deformation — Deformation magnitude (mm)
• All types — Measurement method (free text, e.g. 'UT-A scan', 'caliper')
VALIDATION WARNINGS
• Corrosion without UT or min thickness → soft amber warning (non-blocking)
• Crack without size → soft amber warning
• Deformation without magnitude → soft amber warning

## Slide 23
Screen 22
Evidence
Attach photos before saving the defect record
22 / 29
PURPOSE
• At least one photo is required before saving. Enforces photographic evidence as mandatory.
ACTIONS
• Take Photo — invokes device camera
• Upload Photo — picks from device gallery
• Each evidence item shows a thumbnail placeholder, surface link, and Delete button.
• Save Defect disabled until: location + defect type + severity + ≥1 photo are all set.
PHOTO METADATA
• Each EvidenceItem stores: type, URI, timestamp, GPS (optional), linkedSurface, linkedX, linkedY.

## Slide 24
Screen 23
Defect Saved
Confirmation — record committed to local session
23 / 29
PURPOSE
• Confirms the defect has been saved. Offers natural continuation paths.
SUMMARY CARD
• Shows: defect type · severity · location grid ID · photo count
ACTIONS
• Add Another Defect — keeps the same location, resets defect type; returns to Defect Type screen
• Return to Surface Map — navigates to the Saved Defect Map for the current surface
• Finish Surface — navigates to Surface Review

## Slide 25
Screen 24
Saved Defect Map
Overview of all recorded defects on the current surface
24 / 29
PURPOSE
• Gives a spatial overview of all defects saved so far. Used both during and after defect capture.
MAP COMPONENT — SAME AS LOCATION SELECTION, SURFACE-SPECIFIC
• Shell → ShellSurfaceMap with all defect dots plotted
• Roof → RoofPolarMap with defect dots
• Annular → AnnularTopView with defect zones highlighted
• Nozzle → NozzleClockMap for the selected nozzle
• Bottom → GridMap + MFL status card
ACTIONS
• Add New Defect → Location Mode screen
• Finish Surface → Surface Review

## Slide 26
Screen 25
Surface Review
Per-surface QA before marking complete
25 / 29
PURPOSE
• Summarises the surface inspection and surfaces any blocking issues before the inspector marks it done.
METRICS
• Defect count · Photo count · Grid size · Status (In progress / Complete)
• MFL status card — shown for Bottom surface only
VALIDATION WARNINGS (NON-BLOCKING)
• Defect missing photo
• Bottom surface — no MFL report and no manual observations
• No defects recorded (reminder, not a block)
• One or more defects missing subtype
ACTIONS
• Go Back and Fix → Surface Map
• Mark Surface Complete → Inspection Validation

## Slide 27
Screen 26
MFL Import
Import Magnetic Flux Leakage contractor report — Bottom surface
26 / 29
PURPOSE
• Links the third-party MFL scan report to the inspection record. MFL is the standard method for tank bottom per API 653.
INPUTS
• MFL contractor name
• Report reference number
• Report date
• Scan coverage — Full / Partial (with coverage note if partial)
• Total anomalies flagged
• Overall severity — Clean / Minor findings / Significant findings / Critical findings
• Notes — contractor observations, limitations
ACTIONS
• Save MFL Report → Surface Map with MFL card shown
• Add Manual Observations → Location Mode (for topside manual defects)
• Skip — No MFL Data Yet → Surface Map

## Slide 28
Screen 27
Inspection Validation
Whole-inspection QA before submission
27 / 29
PURPOSE
• Final gate check across the entire inspection session. Submit button is blocked if any warnings exist.
CHECKS PERFORMED
• Tank profile filled in
• Tank orientation set
• Bottom surface complete
• Shell surface complete
• No defects with missing photos
• No defects with invalid coordinates
METRICS PANEL
• Required surfaces complete · Invalid coordinates · Photo requirement — each shows Ready or Needs review
ACTIONS
• Fix Issues → Tank Overview
• Submit Inspection (enabled only when all checks pass) → Export & Summary

## Slide 29
Screen 28
Export & Summary
Executive summary and data export
28 / 29
PURPOSE
• Gives a final report-ready view of the session and provides download options.
SUMMARY SECTIONS
• Inspection header — ID, Tank, Site, Type, Inspector, Date
• Tank profile — Design code, Diameter, Height, Roof type, Shell courses and plate width (if configured)
• Orientation — GPS coordinates, Reference origin, Marker bearing
• Findings — Surfaces done, Total photos, Minor / Moderate / Severe counts, Bottom MFL status
EXPORT FORMATS
• Export JSON package — full session data (all defects, measurements, evidence links, configs)
• Export defect list (CSV) — spreadsheet-ready with columns: ID, Surface, GridID, PlateID, WeldLocation, DefectType, Subtype, Severity, Extent, Description, measurements, Photos, CreatedAt
ACTION
• Confirm & Submit Inspection → Submission Success screen

## Slide 30
Screen 29
Submission Success
Inspection submitted — session queued for sync
29 / 29
PURPOSE
• Final confirmation that the dataset has been committed.
ACTIONS
• View Defect Map — returns to Surface Map
• Start Another Inspection — resets session and goes to Inspection Setup
• Return Home